NIChE – Cherenkov Timing Simulations
A. Ferguson
D. Lahurd
US Analysis Meeting @ CWRU
October, 2013

---
NIChE Prototype

---
Design Principles
- It is natural to think that when the EM component of a shower is at its maximum (Xmax) there will also be a maximum amount of Cherenkov light produced.
- By using the core arrival time (t0) and arrival direction from (for example) the SD and sampling Cherenkov light pulses to establish the atmospheric depth corresponding to the peak of the Cherenkov pulse.

---
L'=√(L2+K2)
Δ = |Z/c - L'/c|
= | Z/c - √(Z2+R2-2R*Z cos(θ) + K2)/c |
Z
L
h
L'
θ
φ
Core
Xp
R
XCh
K
Timing from even one Cherenkov station constrains geometry
And provides a measure of Xmax

---
CORSIKA
- We've generated several 1 EeV showers with no thinning.
- CORSIKA will report the depth of shower maximum in g/cm^2 by taking snapshots of the EM fraction at various depths.
- Can we get the same answer using time of arrival of the Cherenkov wavefront?

---
Time Traces
0.5 km
1.0 km
1.5 km
2.0 km
2.5 km
3.0 km

---
Xmax Reconstruction (Part 1)
Note the strong r dependence of the Xmax reconstruction.
If we tweak the value of t0 used in our reconstruction we can make this go away!

---
Xmax Reconstruction (Part 2)
- Our reconstruction is very sensitive to t0.
- Need to investigate best ways to use SD reconstruction and time-tag Cherenkov pulses.
- Red line corresponds to CORSIKA's “right” answer.

---
Conclusions
- Given an accurate value of t0, we can get a “right answer” for the Xmax for each detector.
- Getting t0 and the value of t for each Cherenkov detector is very important and will likely be a major focus in the immediate future.

---
Work is Ongoing
- Adding wavelength dependence to simulations.
- We will probably need to turn on thinning—need to work on extrapolating from thinned data. Planning on approaching simulations group when we're confident we know what we want.
- Revising fitting techniques for Cherenkov timing pulses.
- Other tasks include estimating trigger rates for various detector configurations.